## Slide 1: MPUs-in-MPLABX-w-MCCH3
Developing bare-metal MCC_Harmony3 applications and debugging in MPLABX
Notes: v1.2: added mchpDeveloperHelp-starting point for at91 (SL, 24.3.23)
v1.1: after dry1/RobG and 2/MattW (14.3.23)
v1.0: first complete version (SL, 30.1.23)

## Slide 2: Class Objectives
Goal of this class is to
  Flow to develop MPU applications with MCC-Harmony and debug in MPLABX (20min=15m+5m demo)
  different at91 variants needed to (20+20min=40min , no/short demo in 40min)
    debug MCCH3 MPU-applications in MPLABX (->let's call variant 'at91_bkptnone') vs
    run MCCH3 MPU-applications in production (->let's call variant 'at91_harmony') vs
    how to extend and debug second level bootloader at91 in MPLABX
  advanced Topics (5min)
  Labs (30min, if time)

## Slide 3: Agenda
Introduction and flow for MPU-H3-apps-in-X (20min)
  How to develop H3 applications for MPUs with MCCH3 + MCC-CM in MPLABX
  Demo: LEDtoggle+PRINTF()
  MCU vs MPU and how MPUs boot
The second level bootloader at91 and how to create it
  Flow for IDE-debugging and production with one MPLABX-prj at91_run.X
    at91_ide (->at91_breaknone) for debugging an MPU-MCCH3-application in MPLABX
    at91_sdc (->at91_harmony_<nvm>) to use an MPU-MCCH3-application in production and sam-ba
  developing/extending at91 in MPLABX -> at91_devel.X
Next step
  H3-drv level and middleware apps and graphics -> MPLABpro: MPUs are first devices that are supported
Labs
  Lab1: LEDtoggle+PRINTF() -> at91 provided
  Lab2a: redo Lab1 but with self-created at91 in MPLABX (->at91_breaknone)
  Lab2b1: Lab1 but with self-created at91 from SDCard (->at91_harmony_<nvm>)
  Lab2b2: Lab1 but with self-created at91 from any embedded NVM (qspi, emmc, nand) (->at91_harmony_<nvm>)
  Lab2c: redo Lab1 but with self-changed at91 from any NVM
Summary

## Slide 4: 1) Introduction & MPU-H3-in-X flow
First let's see a complete flow how to debug H3-apps for MPUs in MPLABX
Second part is about at91, how it's used
  in the MPLABX-based MPU-debug
  in the production environment
  and, finally how to develop/debug at91 sources itself
Goal for this first demo:
  Create simple H3app for SAMA7G54-EK with at91.elf provided ->we'll see in part2 how to create the provided at91.elf ourselves
  FW: LEDtoggle@1Hz + UARTout on console + userButton-press=stopExecution
  HW setup for different/all MPU-boards
  Steps to run demo

## Slide 5: 1) used FW
Three FW functionalities:
LED blinks @SYSTICK=250ms
echo a char on uart-console
  1.char printed is always 'a'
  2.char selected from array charArray with variable char2prntIdx
  print 5x1.char/'a' and 5x'2.char/'b,c,d' (default 'b')
  => changing char2prntIdx shows you can control FW behaviour from the script
on HW-button SW0 press FW
  jumps to endOfTest()
  in endOfTest() print the value of total LEDtoggles stored in finalLedCnt
  and loop there

## Slide 6: 1) Steps to run demo on SAMA7G5-EK
Upfront get infos from DS for SAMA7G5-EK (-> EV21H18A )
  LEDpins: GREEN/PA13 , RED/PB8 , BLUE/PD20 (gpioO,H)
  onboardDbgVCOM: FLX3, IO0/Tx=PD16 , IO1/Rx=PD17
  userButton: PA12 (gpioI, PU)
  memoryView: SRAM-start 0x00100000
tools/options/plugins: set H3framework path + ask-flag
new prj -> MCCH3 prj -> H3path -> prj location,name -> H3cfg -> device -> finish
start MCC -> H3 -> all requ.content avail? -> finish
in H3:
  add STIO->FLEXCOM3 + System/GenTimer@500ms
  pinning from DS (->above)
  GenerateCode
project properties
  debugger: EDBG jlink -> apply
  bootstrap.elf (->Labs\LabHelp\)
  XC32-v4.21 (make sure to use v3x+ as v2.50- have a MPU-specific bug -> hardfault!)
test compile -> add main.c (->Labs\LabHelp\) + re-compile
HWreset -> RomBOOT-msg on console? -> if no, check HWsetup !!
debug-download+run -> notice at91- and h3app-printf on the console

## Slide 7: 1) expected output for demo on SAMA7-EK

## Slide 8: 1) Steps to run demo on SAM9x60-curiosity
Demo for a SAM9x60-curiosity
  LEDpins: RED/PD17, GREEN/PD19 , BLUE/PD21 (gpioO,H)
  onboardDbgVCOM: DBGU, Tx=PA10 , Rx=PA9
  userButton: PA29 (gpioI, PU)
tools/options/plugins: set H3framework path + ask-flag
new prj -> MCCH3 prj -> H3path -> prj location,name -> H3cfg -> device -> finish
start MCC -> H3 -> all requ.content avail? -> finish
in H3:
  add STIO->DBGU + TC1@500ms
  pinning from DS (->above)
  GenerateCode
project properties
  debugger: EDBG jlink -> apply
  bootstrap.elf (->Labs\LabHelp\)
  XC32-v4.21 (make sure to use v3x+ as v2.50- have a MPU-specific bug -> hardfault!)
test compile -> add main.c (->Labs\LabHelp\) + re-compile
HWreset -> RomBOOT-msg on console? -> if no, check HWsetup !!
debug-download+run -> notice at91- and h3app-printf on the console
next slides = step-by-step
for SAM9x60cur
difference MPU vs MCU

## Slide 9: 1) step-by-step for SAM9x60-curiosity (1)
Steps to create+run demo on SAM9x60-curiosity ( EV40E67A )
env: MPLABX-v6.05 MCC-plugin-v5.2.2 XC32-v4.21 SAM9X6_DFP-v1.8.201 or SAMA7G5_DFP-v1.1.175
MPLABX-options: make sure to set H3path AND enable 'always ask...'
H3: prepare/manage H3-repos in either MCC-CM or H3-CM or commandline gitbash ...
0

## Slide 10: 1) step-by-step for SAM9x60-curiosity (2)
Create new MCC-H3 prj (as usual)
1
2
3

## Slide 11: 1) step-by-step for SAM9x60-curiosity (3)
4
5
6
Check MPU-version in DS - eg: on the SAM9x60-curiosity is the SIP 'SAM9x60D1G

## Slide 12: 1) step-by-step for SAM9x60-curiosity (4)
7
8
Start MCC-H3 and you should see 'all required content available'

## Slide 13: 1) step-by-step for SAM9x60-curiosity (5)
9
Pinning SW2 = PA29
LED = R:PD17, G=PD19, B=PD21
vCOM = TX=PA10, RX=PA9 on DBGU
Check DS for pinning

## Slide 14: 1) step-by-step for SAM9x60-curiosity (6)
10
11

## Slide 15: 1) step-by-step for SAM9x60-curiosity (7)
12
Setup prj with J32 & Bootstrap (trick if you don't see 'bootstrap' entry!?)
-> from 'LabHelp\'

## Slide 16: 1) step-by-step for SAM9x60-curiosity (7)
12b
additional/helpful diags-echos if needed without messing with python-script

## Slide 17: 1) step-by-step for SAM9x60-curiosity (8)
MPLABX-v6.05 patches (Jira MPLABX-7342 ->only 9x60!?)
patch ddr.ld-file
add init-step into cstartup.S
add ld-option '--data-init'
13
-> from 'LabHelp\'

## Slide 18: 1) step-by-step for SAM9x60-curiosity (9)
14
HW setup

## Slide 19: 1) step-by-step for SAM9x60-curiosity (10)
15
messages

## Slide 20: 1) expected output on SAM9x60-curiosity (11)
after nReset
at91.elf executes
h3app executes

## Slide 21: 1) various MPU targets
Next we'll look at various MPU-evalkits and the pitfalls each one holds
  SAMA7G5-EK
  SAMA5D2-xplained
  SOM-EK
  WLSOM-EK (with ICD4)
  SAM9x60-EK
  SAM9x60-curiosity
  SAM9x75-ddr3-EB
focus for this session on SAM9x60curiosity -> all other HW-targets are in hidden slides

## Slide 22: 1) HW-setup for demo using SAMA7G54-EK
Debugger and dbgUart choices
Debugger
  use onboard dbg J-Link-OB -> on J24 (microUSB) && Jumper J26=open
  use external dbg J32 -> on J27 (JTAG) && Jumper J26=closed
DebugUART
  use onboard vCOM -> integrated (no extra cable) in J-Link-OB (J24) && Jumper J25=open
  use external vCOM -> extra usb2uart-bridge (eg: FTDI_3v3) on connector DEBUG && Jumper J25=closed
target power
  power: on USBA-connector
Obviously different for each MPU-board BUT tested with
  SOM-EK ->onboardEDBG provides dbg, vCOM and power -> one microUSB-connection
  WLSOM-EK ->usb1 only provides power, need FTDI for vCOM and external debugger
  SAM9x60-EK ->onboardEDBG and vCOM on usb1 and power on usb2
  SAM9x60-cur ->no onboardDbg, nor vCOM, hence need extJ32+FDTI
  SAM9x70-EK ->not tested yet

## Slide 23: 1) HW-setup for demo with SAMA7G-EK
_

## Slide 24: 1) SAMA7G5-EK (works)
SAMA7G5-EK xplained
  HW setup
    Jumpers !!
    nSTART (=pwr button !)
  Prj f2fL1_sama7ek.X
  env
    MPLABX-v6.05.03.6758
    XC32-v4.21
    SAMA5D2_DFP
      (CMSIS-v?? - incl in DFP??)
      DFP-v1.7.172
    Dbg
      typ: EDBG/Jlink
      IF: SWD & JTAG (both work!!)
      speed: 4MHz

## Slide 25: 1) various MPU targets
next we'll look at various MPU-evalkits and the pitfalls each one holds
  SAMA7G5-EK
  SAMA5D2-xplained
  SOM-EK
  WLSOM-EK
  SAM9x60-EK
  SAM9x60-curiosity
  SAM9x75-ddr3-EB

## Slide 26: 1) SAMA5D2* xplained (-)
SAMA5D2* xplained
  HW setup
    Jumpers !!
    not nSTART (=pwr button)
  Prj tc_timer_mode-somek
  env
    MPLABX-v??
    XC32-v??
    SAMA5D2_DFP (CMSIS-v5.8.0)
      v??
    ->so once you have a working env note versions and picture of setup (which connections and jumpers are needed !)
tested before, but not with latest setup
1-20m

## Slide 27: 1) various MPU targets
next we'll look at various MPU-evalkits and the pitfalls each one holds
  SAMA7G5-EK
  SAMA5D2-xplained
  SOM-EK
  WLSOM-EK
  SAM9x60-EK
  SAM9x60-curiosity
  SAM9x75-ddr3-EB

## Slide 28: 1) SAMA5D2* SOM-EK (works)
SAMA5D2* SOM-EK
  HW setup
    Jumpers !!
    not nSTART (=pwr button)
  Prj tc_timer_mode-somek
  env
    MPLABX-v6.05.03.6758
    XC32-v4.21 (v2.50 crashes in hard-fault -> v2.50-bug)
    SAMA5D2_DFP (CMSIS-v5.8.0)
      v1.7.91 works
      v1.9.108 (latest) crashes !!
    ->so once you have a working env note versions and picture of setup (which connections and jumpers are needed !)

## Slide 29: 1) various MPU targets
next we'll look at various MPU-evalkits and the pitfalls each one holds
  SAMA7G5-EK
  SAMA5D2-xplained
  SOM-EK
  WLSOM-EK
  SAM9x60-EK
  SAM9x60-curiosity
  SAM9x75-ddr3-EB

## Slide 30: 1) SAMA5D2* WLSOM-EK (works)
SAMA5D2* WLSOM-EK
  HW setup
    Jumpers !!
    nSTART to route pwr-2-MPU
    no EDBG, need J32
  Prj wlsomblinky
  env
    MPLABX-v6.05.03.6758
    XC32-v4.21 (v2.50 crashes)
    SAMA5D2_DFP (cmsis-v5.8.0)
      v1.9.108 works
      dbgComIF 4w-JTAG
    ->so once you have a working environment note down versions and picture of setup (which connections and jumpers are needed !)

## Slide 31: 1) SAMA5D2* WLSOM-EK + Gen4-ICD4 (works)
SAMA5D2* WLSOM-EK
  HW setup
    Jumpers !!
    nSTART to route pwr-2-MPU
    no EDBG ->Gen4-tools
  Prj wlsomblinky
  env
    MPLABX-v6.05 (-> beta *.03.6758 crashes)
    XC32-v4.21 (v2.50 crashes)
ICD4 -> works
  TP-v1.13.1671
  SAMA5D2_DFP
    DFP-v1.9.106
    cmsis-v5.8.0
  dbgComIF: JTAG
    ->once you've a working environment note down versions and picture of setup (connections, jumpers)
we'll learn later how to find out which Dbg is supported for your MPU-HW

## Slide 32: 1) SAMA5D2* WLSOM-EK + Gen4-ICD4 (works)
expected result with ICD4 (!works!)

## Slide 33: 1) SAMA5D2* WLSOM-EK + Gen4-Pickit4 (fails)
SAMA5D2* WLSOM-EK
  HW setup
    Jumpers !!
    nSTART to route pwr-2-MPU
    no EDBG ->Gen4, next slide
  Prj wlsomblinky
  env
    MPLABX-v6.05 (-> beta *.03.6758 crashes)
    XC32-v4.21 (v2.50 crashes)
Pickit4 -> works
  TP-v1.15.1682
  SAMA5D2_DFP
    DFP-v1.9.106
    cmsis-v5.8.0
  dbgComIF: JTAG
    ->once you've a working environment note down versions and picture of setup (connections, jumpers)

## Slide 34: 1) SAMA5D2* WLSOM-EK + Gen4-Pickit4 (fails)
expected result with ICD4 (!does NOT works!)

## Slide 35: 1) SAMA5D2* WLSOM-EK + Gen5-Pickit5 (fails)
expected result with ICD4 (!does NOT works!)

## Slide 36: 1) various MPU targets
next we'll look at various MPU-evalkits and the pitfalls each one holds
  SAMA7G5-EK
  SAMA5D2-xplained
  SOM-EK
  WLSOM-EK
  SAM9x60-EK
  SAM9x60-curiosity
  SAM9x75-ddr3-EB

## Slide 37: 1) SAM9x60-EK (works)
SAM9x60-EK
  HW setup
    Jumpers !!
    not nSTART (=pwr button)
  Prj tc_timer_mode-sam_9x60_ek_xc32
  env
    MPLABX-v6.05.03.6758
    XC32-v4.21 (v2.50 crashes in hard-fault -> v2.50-bug)
    SAMA9x6_DFP (CMSIS-v5.8.0)
      v1.8.201 (latest) works
    ->so once you have a working env note versions and picture of setup (which connections and jumpers are needed !)

## Slide 38: 1) various MPU targets
next we'll look at various MPU-evalkits and the pitfalls each one holds
  SAMA7G5-EK
  SAMA5D2-xplained
  SOM-EK
  WLSOM-EK
  SAM9x60-EK
  SAM9x60-EK (focus for this session - rest hidden slides)
  SAM9x75-ddr3-EB

## Slide 39: 1) SAM9x60-curiosity (-)
SAMA9x60 curiosity
  HW setup ( EV40E67A )
    J14/15 = DBGU
    nSTART (=pwr button)
  Prj: f2fL1_sam9x60new
  env
    MPLABX-v6.05 (MCC-v5.2.2) (with patches cstartup, ld-file, ld-opt !?)
    XC32-v4.21
    SAMA9x6_ DFP-v1.8.201
    ->so once you have a working environment note versions and picture of setup (which connections and jumpers are needed !)

## Slide 40: 1) various MPU targets
next we'll look at various MPU-evalkits and the pitfalls each one holds
  SAMA7G5-EK
  SAMA5D2-xplained
  SOM-EK
  WLSOM-EK
  SAM9x60-EK
  SAM9x60-curiosity
  SAM9x75-ddr3-EB

## Slide 41: 1) SAM9x75-EB (-)
SAMA9x75 EB
  SAM9x60-curiosity
  SAM9x75-ddr3-EB
  HW setup
    Jumpers !!
    not nSTART (=pwr button)
  Prj -
  env
    MPLABX-v??
    XC32-v??
    SAMA9x7_DFP (CMSIS-v5.8.0)
      v??
    ->so once you have a working env note versions and picture of setup (which connections and jumpers are needed !)
not tested yet

## Slide 42: 1) Various targets - what's the message here?
Don't trust if someone tells you 'it works' or 'should work' -> test yourself, verify AND once you've a working setup !!! note down versions+phy- setup !!!

## Slide 43: DEMO
DEMO on
SAM9x60-curiosity or SAMA7G5-EK with provided at91.elf
or skip ?!
Notes: !!! if time<=15min run demo otherwise skip
!!! prepared demo just loaded=5min -> from-scatch=10min

## Slide 44: 1) summary of steps to run demo on SAMA7G5
Steps to create+run a MPU-H3app
Obviously at91 gets executed, but how?
Following slides will show how at91 is triggered
Demo

## Slide 45: 1) summary of steps to run demo on SAM9x60cur
Steps to create+run a MPU-H3app
Demo
Obviously at91 gets executed, but how? -> following slides show how at91 is triggered
Ran into HardFault?
don't forget to re-compile!
no output? -> baudrate set correctly in plib_dbgu.c ?

## Slide 46: 2) 'a' proper MPU-debug flow
Before we look into how at91 was run, short remark on how to properly debug MPUs in MPLABX:
  in MPLABX setup prjProp with at91_dbg.elf -> open console -> press HW-reset -> make sure to see RomBOOT msg
  on debugDownload make sure you see at91-execution message on console
  use breakpoints, singlestep,... just like normal
  don't use RESET-button in the IDE but instead
    end debug-session with
    press HW-reset on the board -> RomBOOT-msg on console !!
    re-download and restart
  why?
  -> the IDE-reset only reset PC=resetVector, whereas for MPUs it would need to set PC=startApp-in-DDR

## Slide 47: Agenda
Introduction and flow for MPU-H3-apps-in-X
  How to develop H3 applications for MPUs with MCCH3 + MCC-CM in MPLABX
  Demo: LEDtoggle+PRINTF()
  MCU vs MPU and how MPUs boot
The second level bootloader at91 and how to create it (40min)
  Flow for IDE-debugging and production with one MPLABX-prj at91_run.X
    at91_ide (->at91_breaknone) for debugging an MPU-MCCH3-application in MPLABX
    at91_sdc (->at91_harmony_<nvm>) to use an MPU-MCCH3-application in production and sam-ba
  developing/extending at91 in MPLABX -> at91_devel.X
Next step
  H3-drv level and middleware apps and graphics -> MPLABpro: MPUs are first devices that are supported
Labs
  Lab1: LEDtoggle+PRINTF() -> at91 provided
  Lab2a: redo Lab1 but with self-created at91 in MPLABX (->at91_breaknone)
  Lab2b1: Lab1 but with self-created at91 from SDCard (->at91_harmony_<nvm>)
  Lab2b2: Lab1 but with self-created at91 from any embedded NVM (qspi, emmc, nand) (->at91_harmony_<nvm>)
  Lab2c: redo Lab1 but with self-changed at91 from any NVM
Summary
Notes: goal to start this after 20min and this section ~40m

## Slide 48: 2) Resume: steps to create a H3-app and debug in MPLABX
To summarize: to create a H3-application and debug it in MPLABX the steps are
  set path-to-H3framework in Tools/Options/Plugins/MCC + set ask-flag
  create new MCC-H3-prj as usual and select MPU
  start MCC -> best is to make sure all required content is loaded or use MCC-CM to get/update repos
  add functionality/modules in MCC-MHC3 UI -> generate code
  set project properties
    select debugger (->trick 'show all' - later slide)
    bootstrap infos (3 choices: at91-prj or at91.elf or at91.bin + entry&load-addr) -> at91*.elf provided
    XC32-v3.x (before like v2.50 had MPU-specific bug that leads to hard_fault on exec)
  add application and compile
  setup HW, connect console and make sure you see RomBOOT (!? nSTART-button??)
  now dbg-download and notice at91-output on console -> IDE uses DFP\python.scr (details follow!!) to
    extracts at91-name + path and entry/load-address infos from prjProp entry 'bootstrap'
    loads at91 into intSRAM and executes it ->one at91-task is to setup the DDR
    somehow control is given back to IDE to download h3app linked to ddr as in usual MCU-flow
  once h3app is downloaded into DDR, the PC is set to h3app_main() and break or run (->tools/options)
  the IDEreset button only resets PC but doesn't re-run at91, therefore popup warning and not recommended
41-60m

## Slide 49: 2) Summary: review of demo-steps
What did we do in the demo?
=> just created a normal H3app with MCC
What happened in the background?
=> somehow the at91 got executed, but how?
Which memories does the MPU have and what's available after reset?
=> after releasing reset only visible MPU-internal memory is the intSRAM
where did the at91 run from and how was it downloaded?
=> only MPU-memory it can run from is intSRAM, but how was is downloaded+executed
->need some mechanism to download at91 into intSRAM+execute
What is the at91 doing anyway?
=> besides other tasks that at91 initializes the DDR, so it can be used to store+execute code
Where did the application execute?
=> ddr.ld links H3app to DDR, but how was it downloaded?
How did h3app get loaded into DDR?
=> after at91 ran, DDR-space now visible, hence IDE can just download as 'usual'

## Slide 50: 2) Resume: steps to create a H3-app and debug in MPLABX
To summarize: to create a H3-application and debug it in MPLABX the steps are
  set path-to-H3framework in Tools/Options/Plugins/MCC + set ask-flag
  create new MCC-H3-prj as usual and select MPU
  start MCC -> best is to make sure all required content is loaded or use MCC-CM to get/update repos
  add functionality/modules in MCC-MHC3 UI -> generate code
  set project properties
    select debugger (->trick 'show all' - later slide)
    bootstrap infos (3 choices: at91-prj or at91.elf or at91.bin + entry&load-addr) -> at91*.elf provided
    XC32-v3.x (before like v2.50 had MPU-specific bug that leads to hard_fault on exec)
  add application and compile
  setup HW, connect console and make sure you see RomBOOT (!? nSTART-button??)
  now hit IDE dbg-download and notice at91-output on console -> IDE needs some means to download at91 into internalSRAM and execute it -> next section
  once at91 executed DDR-space now visible, hence IDE can just download app as usual in MCU-flow and halt@main (if configured)
  IDEreset button only resets PC but doesn't re-run at91, therefore popup warning and not recommended
41-60m

## Slide 51: 2) how MPUs boot and task of at91
In summary:
Applications for MPUs run out-of DDR
But DDR is setup by at91, hence must first run at91 and only after can load & execute the application
Run from DDR is the usual flow but one can also configure the system to run from eg QSPI with XIP mode and would completely skip DDR ->later slide !
ROMCode
ROMCode
Application
Bootstrap
Application
Bootstrap
Bootstrap
NVM
SAMA5
ROM Memory
SRAM Memory
DRAM
Bootstrap
Valid boot code
Is being executed
Application
Before we look at how at91 is runs, to debug a H3 app in MPLABX, need to understand how MPUs boot?
41-60m

## Slide 52: 2) at91 for H3app develop in MPLABX
Variant needs to support develop&debug of a Harmony3-application in MPLABX
at91 tasks for this case are:
  all at91-tasks like configure PLLs and setup DDR
  finally, just loop@end (->at91_breaknone)
    Before we see how to create this at91-variant in MPLABX, first let's look at how the flow in MPLABX works
41-60m

## Slide 53: 2) MPU-specifics: at91 for H3-dbg in X
What happens in the background when you hit 'Download' in the IDE?
ROM
intSRAM
SAMA7
NVM
DDR
system
4:<dfp>\scripts\jlink*.py: download at91_loopEnd to intSRAM + execute
at91
1: h3app.X prjProp
Bootstrap ->at91*.elf
h3_app.bin
6: MDBCore/IDE: progr_wr() h3app.elf into DDR (as usual)
3: releaseRST
RomBOOT msg?
loop
5: after timeout IDE continues as usual
2:IDE-download: compile h3app.elf
7: jump main() and run
Rom -> no at91? ->sam-ba mode
41-60m

## Slide 54: 2) specifying at91 in MPLABX projectProps
Entry 'bootstrap' in prjProps not visible?
only visible if a debugger that supports MPUs is selected
either connect EDBG/J32 or select via 'Show All' + apply
41-60m

## Slide 55: 2) specifying at91 in MPLABX projectProps
bootstrap in MPLABX project properties:
  use bootstrap 'enable' (why this choice is unclear)
  3 choices
    path to bootstrap project (never tried to use at91…X prj)
    use elf-version of at91 (contains entry-&load-address, so *.elf enough)
    use bin-version of at91, but then need to specify entry- and load-address (-> next slide)
41-60m

## Slide 56: 2) at91 elf vs bin
SAMA7G5
41-60m

## Slide 57: 2) download+execute at91
now know where at91 bootstrap is specified but how is it downloaded into SRAM and executed?
Trick is a python-interface introduced with MPLABX-v5.25 (MPU support was one reason)
With this python-IF all MDBCore functionality is available in python
So, if target=MPU MPLABX loads+executes <DFP>\<mpu>\<version>\scripts\*.py when you hit Download
Let's take a closer look
41-60m

## Slide 58: 2) DFP-python script for at91 (1)
required python-files are from <packs>\<yourArch>\<version>\scripts\<dbg>_<arch>.py eg: <packs>\SAMA7G5_DFP\1.0.56\scripts\j-link_cortex-a7.py
recap from flow on what needs to be done?
-> 1:releaseReset -> 2:download specified at91 into intSRAM -> 3:execute -> 4:give control back to IDE
let's see the relevant parts in the script next -> rest is self-explanatory
41-60m

## Slide 59: 2) DFP-python script for at91 (2)
MPLABX -> MDBcore -> python
re-use MDBCore where possible -> '#mplab' indicates native MDBCore-function
In the 'normal' MCU-flow MDBCore downloads app.elf into MCU-flash on click
fct 'overloading' - eg: def prog_write() [-> MDBCore] vs _prog_write() [-> python]
41-60m

## Slide 60: 2) DFP-python script for at91 (3)
Infos from prjProgs 'bootstrap' are extracted in 'class BootstrapPane():'
User infos on Bootstrap are handled here:
from DFP
41-60m

## Slide 61: 2) DFP-python script for at91 (4)
Function 'def load_file_and_pc(binary_path)' to load at91 and set PC=at91_main()
DFP
to load-at91 & set PC
if at91.elf/hex is provide, it contains entry-+load-addr BUT for at91.bin also need entry- + load-addr
set PC=at91_main() =entry-address
41-60m
Notes: from <packs<\SAMA7G5_DFP\1.0.56\scripts\j-link_cortex-a7.py

## Slide 62: 2) DFP-python script for at91 (5)
All starts with function 'def load_and_run_bootstrap(l_bootstrap_bin)' to load at91 + execute
execute at91 using MDBCore-object reference 'deb'
from DFP
to load & exec at91 (l_bootstrap_bin -> class BootstrapPane():)
use 'load_file_and_pc()' == "load at91 + set PC=at91_main()" ->provious slide
here's where script gives control back to IDE after a timeout
41-60m
Notes: from <packs<\SAMA7G5_DFP\1.0.56\scripts\j-link_cortex-a7.py

## Slide 63: BREAK
BREAK
41-60m

## Slide 64: 2) summary: DFP-python script for at91
<packs<\SAMA7G5_DFP\1.0.56\scripts\j-link_cortex-a7.py
review only major functions as rest is self-explanatory
recap: what needs to be done?
1:releaseReset -> 2:download specified at91 into intSRAM -> 3:execute -> 4:give control back to IDE
all starts with def load_and_run_bootstrap(l_bootstrap_bin)
need to somehow extract the infos provided in prjProp on at91 -> class BootstrapPane()
release reset -> def release_from_reset(): #mplab (!!MDBCore-fct -> fct overloading !!)
download at91 from host (->prjProp/bootstrap-entry) into intSRAM and set PC=at91_main() -> def load_file_and_pc(binary_path) with binary_path -> prjProp/bootstrap-entry
and then downloads at91 byte-by-byte load_binary_file()
and also sets PC -> set_pc(bsEntry) with bsEntry either
  from elf (… if "elf" == filetype: …) via MDBCore-fct deb.PeekSymbolAddress() -> 'deb' is a MDBCore-class exported to python -> MPLABX SDK !!
  or from prjProp/bootstrap-entry if at91.bin specfied
and finally execute downloaded at91 -> dev.GoEx(1,1) -> MDBCore-functionality
what's left?
->must give control back to IDE to download h3app into DDR, as in usual MCU-flow -> timeout
41-60m

## Slide 65: 2) MPUs and supporting debuggers
Debuggers and MPUs - who supports what?
  SAMA7: <X-v6.05>\packs\Microchip\SAMA7G5_DFP\1.0.56\scripts\
    j-link_cortex-a7.py -> SAMA7 supported in MPLABX-v6.05 with Jlink + J32
    - -> not yet supported by Gen4-tools (pickit4, icd4, ice4)
  SAMA5D*: <X-v6.05>\packs\Microchip\SAMA5D2_DFP\1.9.106\scripts\
    j-link_cortex-a5.py -> SAMA5D* supported in MPLABX-v6.05 with Jlink + J32
    icd4_cortex-a5.py -> SAMA5D* supported in MPLABX-v6.05 with ICD4-tools
  SAM9x6: <X-v6.05>\packs\Microchip\SAM9X6_DFP\1.7.85\scripts\
    j-link_arm926ej-s.py -> SAM9X6 supported in MPLABX-v6.05 with Jlink + J32
    - -> not yet supported by Gen4-tools (pickit4, icd4, ice4)
  SAM9x7: <X-v6.05>\packs\Microchip\SAM9X7_DFP\1.0.1\scripts\
    j-link_arm926ej-s.py -> SAM9X7 supported in MPLABX-v6.05 with Jlink + J32
    - -> not yet supported by Gen4-tools (pickit4, icd4, ice4)
41-60m

## Slide 66: 2) at91 variant for H3app develop in MPLABX
Clear how at91 is executed from IDE with the help of <dfp>\*.py
To develop&debug a Harmony3-application in MPLABX at91 tasks are:
  all at91-tasks like configure PLLs and setup DDR
  finally, just loop@end (->at91_breaknone)
    But still don't know to create at91-variants -> let's look at this next
41-60m

## Slide 67: 2) how to create at91 variants in MPLABX?
In the Linux world different at91-versions (like here at91_loopEnd and at91_loadNxtSw) are created with 'make menuconfig'
Ported kConfig into an MPLABX-prj -> see 'at91.X\nbproject\' and 'at91.X\scripts\'
Besides kConfig you also need to cross-compile in MPLABX
due to kConfig being available in MPLABX-prjProps, cannot use this prj.X as 'normal' embedded project to debug at91-sources itself -> how to develop at91 in MPLABX later!
next slides show how to create at91 to run from NVM=SDCard and what changes for other NVMs like eMMC, QSPI,…
important: this at91.X prj is just to configure at91 for your system/NVM and cross-compile BUT not to debug/develop at91-source itself -> 3rd part of this section shows how to do this
41-60m

## Slide 68: 2) how to create at91 variants
Where to start ?
Harmony provides multiple at91-mplabx prjs (all the same !?)
find one for your arch by simply searching the repo csp_apps_<yourArch>
multiple at91-prj (likely all the same never verified!) copy one and start
->next slides show alternative starting-point from mchpDeveloperHelp with lots more details
41-60m

## Slide 69: 2) start from mchpDeveloperhelp (1)
41-60m

## Slide 70: 2) start from mchpDeveloperhelp (2)
41-60m

## Slide 71: 2) start from mchpDeveloperhelp (3)
41-60m

## Slide 72: 2) start from mchpDeveloperhelp (4)
Direct link to microchipDeveloperHelp page: at91-4-MPUs-w-H3-in-MPLABX-on-mchpDevHelp
Basic steps:
Get at91-repository from official MPU32-repo : ()> git clone git://github.com/linux4sam/at91bootstrap.git
For convenience might want to rename the create directory 'at91bootstrap' to 'at91bootstrap.X' so you can immediately see it's an MPLABX project
This repo contains the MPLABX needed files+dirs 'nbproject\' and 'scripts\'
make sure the correct/your MPU is selected in MPLABX-projectProperties
41-60m

## Slide 73: 2) at91 MPLABX project properties
opening such at91.X project, first make sure correct MPU is set and latest DFP is selected
Then notice the different project properties. Instead of typical entries for a MPLABX-prj you only find:
  Makefile -> cross-compile
  Kconfig -> system-configuration
this at91.X prj is just to configure and cross-compile at91 BUT not to debug/develop at91-source itself!
41-60m

## Slide 74: 2) cross-compile at91 with XC32
entry 'Makefile' -> use XC32 to cross-compile the at91 sources
build: make CROSS_COMPILE="C:\Program Files\Microchip\xc32\v4.21\bin\bin\pic32c-"
DebugBuild: make CROSS_COMPILE="C:\Program Files\Microchip\xc32\v4.21\bin\bin\pic32c-"
Clean: make mplabclean CROSS_COMPILE="C:\Program Files\Microchip\xc32\v4.21\bin\bin\pic32c-"
41-60m

## Slide 75: 2) how to create at91 variant in MPLABX
how to create at91-version needed to develop a Harmony3 application in MPLABX?
every H3-csp at91.X project has different configurations in at91*.X\configs\ you can load - eg:
  IDE-usage *_bkptnone_defconfig
  production *<nvm>_<nxtSW>_defconfig
for H3app-debug in MPLABX you need to use <yourMPU>_bkptnone_defconfig
    which does all at91-tasks and then just stops/loops, so IDE can continue
operation
MPU
DDR
Rest leave on default
41-60m

## Slide 76: DEMO
DEMO with self-built at91-4-IDE (change at91-msg printed)
or skip?!
61-70m
Notes: run demo if time <=40min, otherwise
just open at91.X and show how to load defconf
OR skip

## Slide 77: BREAK
BREAK

## Slide 78: 2) at91 to run H3-development in production
What changes if you want to run your H3 application in production ? (NVM = SDcard)
71-90m

## Slide 79: 2) production flow?
clear now how to develop H3application and debug in MPLABX
and clear what at91 tasks are in this case (->at91_loopEnd-4-IDE = 'at91_bkptnone' )
but what to do in production?
at91-tasks are same as for at91_loopEnd_IDE but no IDE to download h3app from host into DDR
like for Linux, at91 needs to load nextSW from NVM into DDR and execute (-> = <arch>_<nextSW>_<nvm>)
eg: sama7g5eksd_harmony_defconfig = for SAMA7G5-EK to boot from SDcard the nextSW='harmony'
can use different NVMs -> see later what changes between NVM=SDCard or =QSPI
next slides shows how the production flow looks like
71-90m

## Slide 80: 5) MPU-specifics: at91 for production
What happens in production?
ROM
intSRAM
SAMA7
NVM=SDCard
DDR
system
1a: SDCard
boot.bin (name fix in ROM!)
4: releaseRST
7: jump main() and run
1b: MPLAB postProc
harmony.bin (how to create?)
2:prep SDCard
2a) manually copy boot.bin+harmony.bin
2b) use sam-ba
at91 on SDCard found (BSCR->BUREG !)
cp to SRAM+exec
PLL, setup DDR,... and copy app to DDR (don't loop!)
at91
h3app.bin
3:plugin SDCard or use sam-ba
at91.bin
harmony.bin
71-90m

## Slide 81: 2) where to load at91 to?
H3app running from DDR, hence need to know DDR-space
from DS find DDR=0x6000.0000->0xE000.0000
can load at91 anywhere, but typically harmony.bin load-address not @start-of-ddr, but with little offset @0x66F0.0000
why not loading harmony.bin to start of DDR=0x6000.0000?
->habit from Linux to load h3app.bin not at DDR-start, but with some offset because first entry typically is uboot
71-90m

## Slide 82: 2) configure at91 for NVM=SDCard
what else is importent?
parameters for SDCard-IF
might come from different datasheets:
  from SAMA7g5-EK datasheet Fig_3-48 you find SDCard on SDMCC-IF SDMMC1
  from SAMA7g5 device DS you find IOset of SDMMC1=IOset1
needed for sam-ba script -> later
71-90m

## Slide 83: 2) configure at91 for NVM=SDCard
don't loop at end but load next SW (eg: h3app.bin)
target = SAMA7G5
load app from SDMMC-IF for SDCard
SDCard on SDHC-IF '1'
SDCard on SDHC-IF '1'
next SW-type, just re-use available entries of 'u-boot'
load nextSW into DDR-space starts 0x6000.0000 (app_ddr.ld !!)
fixed name of nextSW is 'harmony.bin'
at91bootstrap_sam_a7g5_ek.X\configs\sama7g5eksd_harmony_defconfig
71-90m

## Slide 84: 2) harmony.bin
Specific for SDCard with filesystem is that you provide the name of the H3application not the size+loadAddress
default output of XC32-compile is <prj>.elf, so how to create harmony.bin?
Use MPLABX post-processing capability
For SDCard IF the at91 must be named 'boot.bin' (->name fixed in RomCode) -> cross-compile by-default creates multiple versions at91bootstrap*.elf, *.bin, boot.bin…
finally, need to configure BSCR/BUREGs -> next slide
elf:
${MP_CC_DIR}\xc32-objcopy -I elf32-little -O binary "${DISTDIR}/${PROJECTNAME}.${IMAGE_TYPE}.elf" "${DISTDIR}/harmony.bin"
hex:
${MP_CC_DIR}\xc32-objcopy -I ihex -O binary"${DISTDIR}/${PROJECTNAME}.${IMAGE_TYPE}.hex" "${DISTDIR}/${PROJECTNAME}.${IMAGE_TYPE}.bin"
(!!don't copy&paste lines from PPT into MPLABX -> hidden chars!!)
71-90m

## Slide 85: 5) MPU-specifics: at91 for H3-dbg in X
Final steps is to configure BCSR -> at91 sequenceBUREG and BCSR
  possible NVMs are scanned for valid at91
  OTPs mapped to RAM for development eg: SAMA5D2 with BSCR and BUGREG banks !!different for SAMA7 -> BCSR+EMULREG
What is a valid at91?
  Rom reads first 7 vectors (=7*4B/vec =28B) if NVM scanned ->'1'
  6th vector must match at91-size
  7th vector must start with 0xEA or 0xE5 which is a branch/jump
  Now you're finally ready to run yourH3app in production
71-90m

## Slide 86: 2) summary: at91 for SDCard
So to create an at91 to run a H3application in production from SDCard, the steps are
find+copy an at91-prj from H3-csp-<your_architecture>
define cross-compile tools using XC32-executables -> at91.X/projectProperties: Makefile
configure at91 for NVM=SDCard -> at91.X/projectProperties: Kconfig -> load a defconf from at91.X\configs
  primaryOp: load and launch next sw
  Flash-memory: SDCard
  Next SW Type: eg uboot (doesn't matter, just a name!)
  u-boot image storage setup:
    external ram-addr …: 0x66F0.0000 (inside DDR)
    next SW image file name: harmony.bin
link H3app to DDR-space -> ddr.ld linkerfile
SDCard has filesystem, hence you can select H3app by its name 'harmony.bin'
MPLABX-post-processing to create 'harmony.bin
finally might have to configure BCSR/BUREGs (->sam-ba only - cannot be done in MPLABX)
QSPI: does not have filesystem, hence for QSPI need to provide storeAddr and no post-processing -> later slide
71-90m

## Slide 87: DEMO
DEMO with self-built at91-4-SDCard (change at91-msg printed)
skip for 90m-training
71-90m
Notes: run demo if time <=60min, otherwise
just open at91.X and load config 'sd_harmony_defconf'
OR skip
->next section on at91-debug short ~5m

## Slide 88: BREAK
BREAK
71-90m

## Slide 89: 2) sam-ba
Download at91*.bin and h3app.bin into target with sam-ba (BSCR&EMUL must be in RomBOOT-state = sam-ba monitor mode)
#-test sam-ba IF working with readuniqueid
sam-ba -p serial:COM23 -b sama7g5-ek -a readuniqueid
#-use 'help' with any option to get more infos - eg: what 'applets' are known?
sam-ba -p serial:COM23 -b sama7g5-ek -a help
#->Known applets: bootconfig, nandflash, qspiflash, sdmmc -> what commands for bscr-access are known?
sam-ba -p serial:COM23 -b sama7g5-ek -a bootconfig -c help
#->read BSCR/BSC_CR = BootSequenceControl_ConfigRegister
sam-ba -p serial:COM23 -b sama7g5-ek -a bootconfig -c readcfg:bscr
#- Erase QSPI Flash memory
sam-ba -p serial:COM23 -b sama7g5-ek -a qspiflash -c erase
#- Write 'at91_sam9x60cur' (no FS, any name!) to QSPI Flash with offset 0x0 (skip offset == 0ffset=0x0)
sam-ba -p serial:COM23 -b sama7g5-ek -a qspiflash -c writeboot:at91_sam9x60cur.bin
#- Write harmony.bin to QSPI Flash with offset 0x8.0000 (savely after at91)
sam-ba -p serial:COM23 -b sama7g5-ek -a qspiflash -c write:harmony.bin:0x80000
#- use SDCard
#- Write boot.bin (name fix in RomCode) + harmony.bin to SDCard -> #- sdmmc:[<instance>]:[<ioset>]:[<partit>]:[<buswidth>]:[<volt>]
sam-ba -p serial:COM23 -b sama7g5-ek -a sdmmc:1:1:1:4:4 -c write:boot.bin:0x0
sam-ba -p serial:COM23 -b sama7g5-ek -a sdmmc:1:1:1:4:4 -c write:harmony.bin:0x80000
71-90m

## Slide 90: 2) sam-ba
sam-ba docu is in <sam-ba_inst>\doc\index.html
sam-ba docu uses hyperlinks to jump to specific option ->very helpful
71-90m

## Slide 91: 2) at91 config SDcard vs QSPI
SDCard
QSPI
get size of harmony.bin from XC32-compile
NVM-type obviously different
nxtSW is same
QSPI has no filesystem, so must provide addr instead of h3app-name
primary operation same
71-90m

## Slide 92: 2) summary: at91 for production with SDCard
Summary of what must be done to use H3app in production with SDCard
building
  in at91.X project
    configure at91 for SDCard (load-next-SW -> sama7g5eksd_harmony_defconfig)
    specify H3application-name - eg: harmony.bin (!! must match post-processing!!)
    build -> from 'at91. X\build\binaries\' use boot.bin (!fixed name in RomCode!)
  in h3app.X project
    link application for DDR (->ddr.ld)
    add post-processing to create harmony.bin (!! must match at91-config !!)
prepare SDCard
  manually copy boot.bin (->1.a.iii) and harmony.bin (->1.b.ii)
  or use sam-ba to copy both files
run
  don't yet plug SDCard into system -> enable power (nSTART button) -> open console + HWreset -> make sure you see 'RomBOOT' msg (no need to continue if no RomBOOT-msg BUT check setup)
  now plug SDCard into system and reset -> you should see at91-msg and h3app-msg on the console
71-90m

## Slide 93: 2) summary: at91 for production with QSPI
Summary of what must be done to use H3app in production with QSPI
building
  in at91.X project
    configure at91 for SDCard (load-next-SW -> sama7g5ekdf_qspi_uboot_defconfig)
    no fileSystem on QSPI, hence can't specify h3app by name 'harmony.bin' but with h3app-size (->1.b.iii)
    build -> from 'at91. X\build\binaries\' use in project-properties entry 'Bootstrap' at91bootstrap.bin or boot.bin
  in h3app.X project
    link application for DDR (->ddr.ld)
    post-processing still needed to create binary but no specific name, though need h3app-size
    compile to get h3app.bin and h3app-size
prepare QSPI
  use sam-ba to program 'at91bootstrap.bin' (->1.a.iii) and 'h3app.bin' (->1.b.iii) using h3app-size (->1.b.iii) and also define h3app-offset (whatever fits)
run
  open console -> should see 'RomBOOT' msg and immediately at91 and then h3app
71-90m

## Slide 94: Agenda
Introduction and flow for MPU-H3-apps-in-X
  How to develop H3 applications for MPUs with MCCH3 + MCC-CM in MPLABX
  Demo: LEDtoggle+PRINTF()
  MCU vs MPU and how MPUs boot
The second level bootloader at91 and how to create it
  Flow for IDE-debugging and production with one MPLABX-prj at91_run.X
    at91_ide (->at91_breaknone) for debugging an MPU-MCCH3-application in MPLABX
    at91_sdc (->at91_harmony_<nvm>) to use an MPU-MCCH3-application in production and sam-ba
  developing/extending at91 in MPLABX -> at91_devel.X
Next step
  H3-drv level and middleware apps and graphics -> MPLABpro: MPUs are first devices that are supported
Labs
  Lab1: LEDtoggle+PRINTF() -> at91 provided
  Lab2a: redo Lab1 but with self-created at91 in MPLABX (->at91_breaknone)
  Lab2b1: Lab1 but with self-created at91 from SDCard (->at91_harmony_<nvm>)
  Lab2b2: Lab1 but with self-created at91 from any embedded NVM (qspi, emmc, nand) (->at91_harmony_<nvm>)
  Lab2c: redo Lab1 but with self-changed at91 from any NVM
Summary
71-90m

## Slide 95: 2) at91 for development/extention
In this section we'll look at how to debug/extent the at91
71-90m

## Slide 96: 2) at91 development
final task is to extend/develop at91 itself in MPLABX -> need proper MPLABX prj
With at91.X-project we used before, can configure at91 and cross-compile for 2 cases
  H3-app development in MPLABX-IDE (= loop@end -> 'at91_bkptnone')
  H3-app execution in production (= loadNextSW_from_NVM -> 'at91_harmony_<nvm>')
BUT this at91.X projects from H3 are not 'normal' embedded-MPLABX projects, hence missing prjProps like XC32-v, Debugger, … because the prjProp are 'misused' for cross-compile and kConfig
somehow you need to add the at91-sources into an embedded project
there're two basic choices
  either create an embedded MPLABX-prj from scratch and manually cp at91.X-sources
  or simply use the *.elf from the H3-at91.X prj in a MPLABX-prebuild-prj
71-90m

## Slide 97: 2) at91 development: manually copy at91*.c/h
create new H3-prj and manually copy sources + cross-compile-calls -> but which sources need to be copied and what options are used?
just use the compiler log
you think it painful? Well, yes recall how often, you'd do this?
exactly, only once when you define your system !
but clearly the next solution (=prebuild.elf) is the better way
sources you need to copy
compiler-version
assembler-options
compile-options
linker-options
71-90m

## Slide 98: 2) at91 development: manually copy at91*.c/h
steps to create a new MPLABX-project for at91
use IDE-option 'file/add existing item from folder' && 'filter for *.h' or '*.c' respectively
71-90m

## Slide 99: 2) at91 development: prebuild flow
Steps for the prebuild-prj flow
create separate/new MPLABX-prebuild and use at91*.elf created in '1'
for every change in sources in at91.X-prj use reload elf in prebuild-project
press HWreset -> check 'RomBOOT' msg on console
now set breakpoint in source-code of orig at91.X-project BUT from the at91_prebuild.X prj
71-90m

## Slide 100: 2)Summary: at91
different variants of at91
  loop@end for IDE-development of H3-application
  loadNextSW for production -> differences between NVMs
    SDCard
      uses h3-name (eg: harmony.bin) in kConfig, hence need MPLABX post-processing step
      and at91 must be named boot.bin because named fixed in RomCode
    QSPI
      need size-of-h3app and specify in kConfig
      also need to specify flash-storage-address of h3app (no post-processing)
BSCR and BUREG/EMUL registers, like on Linux to configure boot sequence
download at91+h3app for production either manually (->SDCard) or with sam-ba
debug/extend at91 use 2 projects,
  project1, eg: at91_cfg.X, where you configure + cross-compile (kConfig!) at91
  project2, eg: at91_preb-dev.X, as prebuild-elf, which references at91*.elf from project1/at91_cfg.X
71-90m

## Slide 101: BREAK
BREAK

## Slide 102: Agenda
Introduction and flow for MPU-H3-apps-in-X
  How to develop H3 applications for MPUs with MCCH3 + MCC-CM in MPLABX
  Demo: LEDtoggle+PRINTF()
  MCU vs MPU and how MPUs boot
The second level bootloader at91 and how to create it
  Flow for IDE-debugging and production with one MPLABX-prj at91_run.X
    at91_ide for debugging an MPU-MCCH3-application in MPLABX
    at91_sdc to use an MPU-MCCH3-application in production and sam-ba
  developing/extending at91 in MPLABX -> at91_devel.X
Next step
  H3-drv level and middleware apps and graphics -> MPLABpro: MPUs are first devices that are supported
Labs
  Lab1: LEDtoggle+PRINTF() -> at91 provided
  Lab2a: redo Lab1 but with self-created at91 in MPLABX
  Lab2b1: Lab1 but with self-created at91 from SDCard
  Lab2b2: Lab1 but with self-created at91 from any embedded NVM (qspi, emmc, nand)
  Lab2c: redo Lab1 but with self-changed at91 from any NVM
Summary
Notes: next section only 5min without running the usb-demo but

## Slide 103: 3) Next steps
System choices
  you can configure QSPI-IF into XIP, hence system=MPU+QSPI but no DDR (cost!?)
    change at91 to setup all but DDR
    at91 should at the end, instead of DDR-setup, change QSPI-IF into XIP
    and then reset and set PC to qspi_main()
  drawback
    QSPI-performance much lower then DDR-performance
    QSPI: 50MHz on 4xdatalines -> 200b/s vs DDR: 266*2(doubleDataRate)=532*32b=…17kb/s
L2-cache
  on SAMA5D* can configure L2-cache (256kB) to be added to intSRAM (128kB), so SAMA5 can have 384kB-intSRAM - not possible on SAMA7 and SAM9x6/7x
71-90m

## Slide 104: 3) Harmony next level
Harmony3 provides various drv- and middleware examples
  DriverLevel = <h3>\core_apps_sam_a7g5\apps\: i2c , i2c_eeprom, spi, spi_eeprom, usart
  Crypto =
    <h3>\crypto_apps_large_hash\apps\large_hash
    <h3>\crypto_apps_encrypt_decrypt\apps\encrypt_decrypt
  GFX = <h3>\gfx_apps_sam_a5d2 -> separate EGT-session
  Net = <h3>\net_apps_sam_a5d2
  USB =
    <h3>\usb_apps_device = msd_sdcard , cdc_com_port_single, …
    <h3>\usb_apps_host = hid_basic_keyboard, msd_basic, …
    => USB-example on next slide
  Wireless = …
71-90m

## Slide 105: 3) Harmony next level: usb
H3-USB example
prj f2fL3_usb--cdc_msd_sdcard-sama7_only
prepare demo
  physical setup on the right
  cp <h3>\usb_apps_device\apps\cdc_msd_sdcard\
  prjProp
    SAMA7G5-DFP_v1.1.175, XC32-v4.21
    select your at91-4-ide - eg: <ESI_F2F>\Labs\LabHelp\sama7g5_at91bootstrap.elf
    set brkpt in 'case APP_STATE_INIT' (->not sure, but demo only works with this brkpt!) and enable 'halt@main' in tools/options/embedded
running demo
  open console and make sure you see 'RomBOOT' msg
  now download&debug <cdc_msd_sdcard> prj and stop@main (LED=green)
  hit continue to run to brkpt on 'case APP_STATE_INIT' (LED=off)
  hit continue (you'll hear usb-enumeration-bingBong and LED=green)
  open 2.console on CDC-USBport and press user button to see 'PUSH BUTTON PRESSED' -> next slide for expected result
71-90m

## Slide 106: 3) Harmony next level: usb -> expected result
71-90m

## Slide 107: Agenda
Introduction and flow for MPU-H3-apps-in-X
  How to develop H3 applications for MPUs with MCCH3 + MCC-CM in MPLABX
  Demo: LEDtoggle+PRINTF()
  MCU vs MPU and how MPUs boot
The second level bootloader at91 and how to create it
  Flow for IDE-debugging and production with one MPLABX-prj at91_run.X
    at91_ide for debugging an MPU-MCCH3-application in MPLABX
    at91_sdc to use an MPU-MCCH3-application in production and sam-ba
  developing/extending at91 in MPLABX -> at91_devel.X
Next step
  H3-drv level and middleware apps and graphics -> MPLABpro: MPUs are first devices that are supported
Labs
  Lab1: LEDtoggle+PRINTF() -> at91 provided
  Lab2a: redo Lab1 but with self-created at91 in MPLABX
  Lab2b1: Lab1 but with self-created at91 from SDCard
  Lab2b2: Lab1 but with self-created at91 from any embedded NVM (qspi, emmc, nand)
  Lab2c: redo Lab1 but with self-changed at91 from any NVM
Summary
90-95m

## Slide 108: Lab help files
dummy empty files just as separator
H3-application (copy+rename to main.c)
MPLABX-v6.05 patch files
defconfig files for SAM9x60curiosity (might be missing, depending on which H3-at91.x project you start with
for SAM9x60curiosity:
  at91-variants
    at91_4_ide=*_bkptnone* ->loop@end
    at91_4_sdc0=*_sdc0_harmony* ->loadNxtSW
  harmony.bin
for SAMA7G5-EK
90-100m

## Slide 109: Lab1
ENV: MPLABX-v6.05+, XC32-v4.21, DFP_SAMA7G5-v1.1172
Now do this basic lab yourself -> 'Labs\LabHelp\' has 'main.c' and 'at91.elf'
you should see below output on console & RBG-LED toggle & stop with SW1
Pitfall: wrong 'device' set / prj-DFP+-XC32 version not installed -> MPLABX just switches to latest DFP
at91*.bin but forgot to set entry/load-addr

## Slide 110: Lab2a: at91 for H3-debug in MPLABX (SAM7G5)
Lab with second level bootloader at91: first build at91 from at91-MPLABX-prj to debug an H3-app in X
->start from 'a' H3-prj as shown before
    at91 for debugging an MPU-MCCH3-application in MPLABX -> at91_4_ide
      Lab2a: redo Lab1 but with self-created at91 in X
    at91 to use an MPU-MCCH3-application in production and sam-ba
      Lab2b1: Lab1 but with self-created at91 from SDCard
      (Lab2b2: Lab1 but with self-created at91 from any embedded NVM (qspi, emmc, nand -> need to handle BSCR+BUREG + clear NVM again)
=>expected output
at91_4_ide
at91_4_ide
change at91-&h3app printf() in at91bootstrap_sam_a7g5_ek.X\device\sama7g5\sama7g5.c

## Slide 111: Lab2a: at91 for H3-debug in MPLABX (SAM9x60cur)
Lab with second level bootloader at91: first build at91 from at91-MPLABX-prj to debug an H3-app in X
->start from 'a' H3-prj as shown before
    at91 for debugging an MPU-MCCH3-application in MPLABX -> at91_4_ide
      Lab2a: redo Lab1 but with self-created at91 in X
    at91 to use an MPU-MCCH3-application in production and sam-ba
      Lab2b1: Lab1 but with self-created at91 from SDCard
      (Lab2b2: Lab1 but with self-created at91 from any embedded NVM (qspi, emmc, nand -> need to handle BSCR+BUREG + clear NVM again)
=>expected output
at91_4_ide
at91_4_ide
change at91-&h3app printf() in at91bootstrap_sam_a7g5_ek.X\driver\board_hw_info.c

## Slide 112: Lab2b: at91 for H3-app in production with SDCard (SAMA7G5)
Lab with second level bootloader at91 -> Flow for IDE-debugging and production
    at91 for debugging an MPU-MCCH3-application in MPLABX
      Lab2a: redo Lab1 but with self-created at91 in X
    at91 to use an MPU-MCCH3-application in production and sam-ba -> at91_4_sdc
      Lab2b1: Lab1 but with self-created at91 from SDCard
      (Lab2b2: Lab1 but with self-created at91 from any embedded NVM -> to use qspi, emmc, nand -> need to handle BSCR+BUREG + clear NVM again -> try yourself)
=>expected output
change at91-&h3app printf() in at91bootstrap_sam_a7g5_ek.X\device\sama7g5\sama7g5.c

## Slide 113: Lab2b: at91 for H3-app in production with SDCard (SAM9x60c)
Lab with second level bootloader at91 -> Flow for IDE-debugging and production
    at91 for debugging an MPU-MCCH3-application in MPLABX
      Lab2a: redo Lab1 but with self-created at91 in X
    at91 to use an MPU-MCCH3-application in production and sam-ba -> at91_4_sdc
      Lab2b1: Lab1 but with self-created at91 from SDCard
      (Lab2b2: Lab1 but with self-created at91 from any embedded NVM -> to use qspi, emmc, nand -> need to handle BSCR+BUREG + clear NVM again -> try yourself)
=>expected output
change at91-&h3app printf() in at91bootstrap_sam_a7g5_ek.X\driver\board_hw_info.c

## Slide 114: Lab2c) at91 development (SAMA7G5)
Debug at91 sources with either method
a: create new mplab.prj and manually copy src+h+options
b: prebuild-elf
  to proof you really use the sources from the prebuild-prj change sth in at91-source eg: sama7g5.c L1205dbg_print(…) and recompile at91
  Lab2c: change at91 and re-do Lab1 with self-changed at91
change at91-&h3app printf() in at91bootstrap_sam_a7g5_ek.X\device\sama7g5\sama7g5.c
at91_4_develop

## Slide 115: Lab2c) at91 development (SAM9x60cur)
Debug at91 sources with either method
a: create new mplab.prj and manually copy src+h+options
b: prebuild-elf
  to proof you really use the sources from the prebuild-prj change sth in at91-source eg: sama7g5.c L1205dbg_print(…) and recompile at91
  Lab2c: change at91 and re-do Lab1 with self-changed at91
change at91-&h3app printf() in at91bootstrap_sam_a7g5_ek.X\driver\board_hw_info.c
at91_4_develop

## Slide 116: Agenda
Introduction and flow for MPU-H3-apps-in-X
  How to develop H3 applications for MPUs with MCCH3 + MCC-CM in MPLABX
  Demo: LEDtoggle+PRINTF()
  MCU vs MPU and how MPUs boot
The second level bootloader at91 and how to create it
  Flow for IDE-debugging and production with one MPLABX-prj at91_run.X
    at91_ide for debugging an MPU-MCCH3-application in MPLABX
    at91_sdc to use an MPU-MCCH3-application in production and sam-ba
  developing/extending at91 in MPLABX -> at91_devel.X
Next step
  H3-drv level and middleware apps and graphics -> MPLABpro: MPUs are first devices that are supported
Labs
  Lab1: LEDtoggle+PRINTF() -> at91 provided
  Lab2a: redo Lab1 but with self-created at91 in MPLABX
  Lab2b1: Lab1 but with self-created at91 from SDCard
  Lab2b2: Lab1 but with self-created at91 from any embedded NVM (qspi, emmc, nand)
  Lab2c: redo Lab1 but with self-changed at91 from any NVM
Summary

## Slide 117: overall summary: review of demo-steps
H3-application creation as normal for other MCUs
MPUs don't have internal flash, but only intSRAM -> hence somehow need to setup DDR and load h3app-image from NVM into DDR
This is done by at91 and DFP-python scripts
  for MPLABX-debug-flow DFP-python-scripts load+execute at91 - once done IDE can download h3app as normal for other MCUs into DDR, now visible -> no means for at91 to tell MPLABX 'I am done', just timeout -> at91-for-ide = at91 that does all at91-tasks, but then loop@End -> at91_bkptnone
  for production at91 is stored on NVM, loaded by ROMcode and executed and finally loads h3app into DDR and executes it -> at91-for-production = at91 the does all at91-tasks BUT then loads nextSW -> = <arch>_<nextSW>_<nvm>
  python scripts in <dfp-pack>\Microchip\SAMA7G5_DFP\1.0.56\scripts\
    all starts with function def load_and_run_bootstrap(l_bootstrap_bin) - use MDBCore-functionality where possible
    supported debugger -> <debugger>_<arch>.py - eg: j-link_cortex-a5.py = SAMA5D* supported by Jlink/J32
Need to provide at91*.elf project properties (trick 'show all' or connect J32)
three choices to use at91*.elf for H3app-debug in MPLABX: at91-project, at91.elf, at91.bin (load+startAddr)

## Slide 118: overall summary: review of demo-steps
at91.X projects available, either search 'at91*.X' in <h3>\csp_apps_<arch>\apps or get from git://github.com/linux4sam/at91bootstrap.git => let's call this at91_cfg.X
use prepared *_defconfig files from at91.X\configs\ to create at91-for-production -> <arch>_<nextSW>_<nvm> eg: sama7g5eksd_harmony_defconfig = for SAMA7G5-EK to boot from SDcard the nextSW='uboot'
at91-projects
  use one at91_cfg.X with kConfig to configure & cross-compile at91 (-> see above)
  use second prebuild-elf-project at91_dev.X to develop at91 itself and just reference at91*.elf from at91_cfg.X
Each NVM might have specifics, like SDCard: provide h3app-name (->harmony.bin -> use MPLABX-post-processing step)
default h3-application space is DDR, but can also run from QSPI
H3-application linked into DDR -> h3app.ld
IDE-reset button not working as it only resets PC=resetVector but not DDR-h3app-startAddr -> proper debug-flow: use brkpt,single,… as usual BUT instead of IDE-reset, end dbgSession and restart all over
make sure to see 'RomBOOT' msg before you start downloading
XC32-v2.5x had issues specific to MPUs - execution would end in hard-fault
START buttons on some MPU-boards - only once pressed power routed to MPU

## Slide 119: Questions?

## Slide 120: Dev Tools For This Class
HW
  SAMA7G54-EK (has EDBG and vCOM on board)
  2 Micro-USB cable
SW
  MPLABX-v6.05+
  XC32-v4.21+
  MCC-v5.2.2
inWork

## Slide 121: LEGAL NOTICE
SOFTWARE:
You may use Microchip software exclusively with Microchip products. Further, use of Microchip software is subject to the copyright notices, disclaimers, and any license terms accompanying such software, whether set forth at the install of each program or posted in a header or text file.
Notwithstanding the above, certain components of software offered by Microchip and 3rd parties may be covered by “open source” software licenses – which include licenses that require that the distributor make the software available in source code format. To the extent required by such open source software licenses, the terms of such license will govern.
NOTICE & DISCLAIMER:
These materials and accompanying information (including, for example, any software, and references to 3rd party companies and 3rd party websites) are for informational purposes only and provided “AS IS.” Microchip assumes no responsibility for statements made by 3rd party companies, or materials or information that such 3rd parties may provide.
MICROCHIP DISCLAIMS ALL WARRANTIES, WHETHER EXPRESS, IMPLIED, OR STATUTORY, INCLUDING ANY IMPLIED WARRANTIES OF NONINFRINGEMENT, MERCHANTABILITY, AND FITNESS FOR A PARTICULAR PURPOSE. IN NO EVENT WILL MICROCHIP BE LIABLE FOR ANY DIRECT OR INDIRECT, SPECIAL, PUNITIVE, INCIDENTAL, OR CONSEQUENTIAL LOSS, DAMAGE, COST, OR EXPENSE OF ANY KIND RELATED TO THESE MATERIALS OR ACCOMPANYING INFORMATION PROVIDED TO YOU BY MICROCHIP OR OTHER THIRD PARTIES, EVEN IF MICROCHIP HAS BEEN ADVISED OF THE POSSIBLITY OF SUCH DAMAGES OR THE DAMAGES ARE FORESEEABLE. PLEASE BE AWARE THAT IMPLEMENTATION OF INTELLECTUAL PROPERTY PRESENTED HERE MAY REQUIRE A LICENSE FROM THIRD PARTIES.
TRADEMARKS:
The Microchip name and logo, the Microchip logo, Adaptec, AnyRate, AVR, AVR logo, AVR Freaks, BesTime, BitCloud, chipKIT, chipKIT logo, CryptoMemory, CryptoRF, dsPIC, FlashFlex, flexPWR, HELDO, IGLOO, JukeBlox, KeeLoq, Kleer, LANCheck, LinkMD, maXStylus, maXTouch, MediaLB, megaAVR, Microsemi, Microsemi logo, MOST, MOST logo, MPLAB, OptoLyzer, PackeTime, PIC, picoPower, PICSTART, PIC32 logo, PolarFire, Prochip Designer, QTouch, SAM-BA, SenGenuity, SpyNIC, SST, SST Logo, SuperFlash, Symmetricom, SyncServer, Tachyon, TempTrackr, TimeSource, tinyAVR, UNI/O, Vectron, and XMEGA are registered trademarks of Microchip Technology Incorporated in the U.S.A. and other countries.
APT, ClockWorks, The Embedded Control Solutions Company, EtherSynch, FlashTec, Hyper Speed Control, HyperLight Load, IntelliMOS, Libero, motorBench, mTouch, Powermite 3, Precision Edge, ProASIC, ProASIC Plus, ProASIC Plus logo, Quiet-Wire, SmartFusion, SyncWorld, Temux, TimeCesium, TimeHub, TimePictra, TimeProvider, Vite, WinPath, and ZL are registered trademarks of Microchip Technology Incorporated in the U.S.A.
Adjacent Key Suppression, AKS, Analog-for-the-Digital Age, Any Capacitor, AnyIn, AnyOut, BlueSky, BodyCom, CodeGuard, CryptoAuthentication, CryptoAutomotive, CryptoCompanion, CryptoController, dsPICDEM, dsPICDEM.net, Dynamic Average Matching, DAM, ECAN, EtherGREEN, In-Circuit Serial Programming, ICSP, INICnet, Inter-Chip Connectivity, JitterBlocker, KleerNet, KleerNet logo, memBrain, Mindi, MiWi, MPASM, MPF, MPLAB Certified logo, MPLIB, MPLINK, MultiTRAK, NetDetach, Omniscient Code Generation, PICDEM, PICDEM.net, PICkit, PICtail, PowerSmart, PureSilicon, QMatrix, REAL ICE, Ripple Blocker, SAM-ICE, Serial Quad I/O, SMART-I.S., SQI, SuperSwitcher, SuperSwitcher II, Total Endurance, TSHARC, USBCheck, VariSense, ViewSpan, WiperLock, Wireless DNA, and ZENA are trademarks of Microchip Technology Incorporated in the U.S.A. and other countries.
SQTP is a service mark of Microchip Technology Incorporated in the U.S.A.
The Adaptec logo, Frequency on Demand, Silicon Storage Technology, and Symmcom are registered trademarks of Microchip Technology Inc. in other countries.
GestIC is a registered trademark of Microchip Technology Germany II GmbH & Co. KG, a subsidiary of Microchip Technology Inc., in other countries.
All other trademarks mentioned herein are property of their respective companies.
© 2019, Microchip Technology Incorporated, All Rights Reserved.

## Slide 122: Backup

## Slide 123: 1) step-by-step for SAM9x60-curiosity (10)
14b
MPLABX-prj: Labs\gh_esi_f2f_ww_2023\f2fL1_sam9x60\f2fL1_sam9x60new\firmware\f2fL1_sam9x60_cur.X
configs (->Labs\f2fL2_at91\at91bootstrap_sam_9x60_ek.X)
IDE-loop configs: sam9x60_curiosity_bkptnone_defconfig
SDC0 (=uSD) configs: sam9x60_curiosity_sdc0_harmony_defconfig